## Slide 1
Identification of land cover change in high-speed rail (HSR) station area through latent class analysis with covariates:
Findings for the Yangtze River Delta region
Xinyi WANG (presenter) PhD Candidate, Department of Urban Planning, Tongji University, China, xywang_@tongji.edu.cn
Haixiao PAN*, Ph.D. Professor, Department of Urban Planning, Tongji University, China, hxpank@126.com
Ya GAO, Ph.D. Postdoctoral Fellow, Department of Civil & Mineral Engineering, University of Toronto, Canada, lucia.gao@mail.utoronto.ca
ENPC, PARIS, FRANCE
07 November, 2024
Forum THNS2024: TRANSFORMING TRANSPORT
Session 7: Transport and the environment
Notes: Thank you Mr. SHI for giving me the flow. Good morning and good afternoon, everyone!
My name is Xinyi Wang, and I’m a PhD candidate in the Department of Urban Planning at Tongji University. It’s my great honor on behalf of our team to share the latest findings here. The title is: Identification of land cover change in high-speed rail (HSR) station area through latent class analysis with covariates: Findings for the Yangtze River Delta region.

## Slide 2
Chart: Accumulated Mileage of China's HSR (km)
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Accumulated Mileage/km | 404 | 404 | 404 | 404 | 404 | 1035 | 3384 | 5487 | 7027 | 10111 | 13670 | 19621 | 24367 | 26704 | 28560 | 32610 | 36895 | 39415 | 41583
404
41,583
Accumulated Mileage of China’s HSR
Territorial spatial planning of Hongqiao International CBD, Shanghai (Hongqiao HSR Station Area)
R = 1km
Introduction
The first High-Speed Rail (HSR) line in China was opened in 2003 --> the world’s longest HSR network.
Previous researches on HSR and land development around stations found that the development on HSR could bring about the prosperity of the locational area, the economy growth and the development around the station area to a great extant.
Early evidence in European cities showed that the development of HSR would also make the HSR station areas more attractive.
HSR station as a catalyst in urban development.
我国的广域高速铁路网络
现有研究主要关注两个空间层次，一是对城市or区域、二是对车站周边
高铁站对车站周边地区的开发
为什么要关注这个是因为……，回顾过去20年的发展历程，
我国的高铁站建设方式：郊外新建（多）、内城更新（少）
划定影响范围
这篇研究想要解决的三个问题
Notes: Firstly, I will give a brief introduction about the background of HSR in China. The first HSR line in China was opened in 2003, and till now, it has become the world’s longest HSR network.
Previous researches have found that the development on HSR could bring about the prosperity of the locational area, the economy growth and the development around the station area to a great extant.
Some European experience showed that the development around the HSR station would make the station areas more attractive.

## Slide 3
Introduction
Initially in China, new HSR stations were designed to bring new development in new towns (HSR New Cities).
When reviewing the process of HSR construction in the past two decades, it had been gradually found that not each HSR station was capable to bring about new construction lands around as planned.
Station
Address
HSR Lines
Status
Not into operation after completion
Closed after a temporary use
Closed after a temporary use due to the less passenger flows: Huaqiao Station
Vacant in 16 years before it was into operation in Sep 2024 (Yizhuang Station, Beijing)
Yizhuang, Beijing, 2008
Yizhuang, Beijing, 2024
Huaqiao, Suzhou, 2018
Notes: Well, with so many HSR stations in China, a majority of newly built HSR stations were designated to bring new development around the stations, that is called HSR New Cities. But we could find that the operation states of some station doesn’t match what we have imagined in the planning process.
Here lists some stations that has never been into operation after completion, or being closed after a temporary use.

## Slide 4
Introduction
The changes of HSR on land development in station area
(3) What factors contribute to the disparities of different land cover changes?
(2) What are the characteristics of identifying different land cover change patterns of the station areas?
(1) Is the development around the HSR stations compact and effective? and how to measure the land cover changes comprehensively from the greenfield to the built-up land in the station areas?
Notes: So under these circumstances, we would like to put forward these research question:
Firstly, we would like to investigate whether the development around the HSR stations compact and effective, and how to measure the land cover changes comprehensively from the greenfield to the built-up land in the station areas?
Secondly, …, and lastly, …

## Slide 5
Literature Review
The changes of HSR on land development in station area
Tokyo, Japan (~ 6.5 km)
Tokyo Station
Shinagawa Station
Ueno Station
CITY CENTER
Shanghai, China (up to 15 km)
Shanghai Rwy. Sta.
(Upgraded in 1987)
Shanghai South Rwy. Sta.
(Upgraded in 2006)
Hongqiao Rwy. Sta.
(newly built in 2010)
CITY CENTER
Paris, France (~ 4.0 km)
Paris Nord
Paris-Est
Gare de Lyon
Paris-Montparnasse
CITY CENTER
1）高速铁路对车站地区土地开发的影响
溢出效应：
规模 – 更多的建设用地
功能 – 不同类型产业的聚集
结构 – 有些成为新的中心、而有的没有
The agglomeration of built-up lands around the HSR station
(Spillover effect)
At the dimension of land use scale and form:
The accumulation of more built-up lands (Coronado et al., 2019).
The places where the land renewal occurred (Chen et al., 2019).
At the dimension of urban function [mainly from the micro scale]:
Reflected in the agglomeration of different types of industries (Ilie, 2014).
Typically, commercial and service facilities are concentrated in the central station area, while the industrial manufacturing industry is more likely to concentrate in the peripheral station area (Beckerich et al., 2019).
At the dimension of urban structure [mainly from the macro scale]:
Some of the station area have gradually become one of the important urban activity zones (Gong & Li, 2022).
Stations adjacent to CBD could enhance the redevelopment of city center, leading to agglomeration of enhanced business and commercial services (Kim et al., 2018).
Notes: The changes of HSR on land development in station area was typically called the spillover effect of the HSR station. It mainly lies in the following three dimensions.
At the dimension of land use scale and form, it is obvious to accumulate the built-up lands and populations.
At the dimension of urban function, the different location of stations could gather different types of industries.
And the top two dimensions are what we will discuss in the following studies.

## Slide 6
Literature Review
Contributing factors on land cover change
2）土地覆盖变化的原因
A) 高铁站所在城市的社会经济属性socioeconomic attributes
B) 高铁站的区位 the locational attributes
C) 高铁站所在的高铁网络属性
Three types of contributing factors
The factors in urban social economy:
It was found that the larger the residential population scale or the higher the economic level, the stronger the potential of the station city to lead the development around the HSR station (Wang et al., 2019).
The factors in HSR station location:
It typically contains both the geographical distance and the accessibility between the station and city centers.
In most cases, the stations in the outskirts were designated to stimulate new urban growth or complementary sub-centers to escape from the old city, while those in the downtown area were assigned to reinforce the existing urban centers (Hall, 2009; Yin et al., 2015).
Inhibit the development potential of the station areas, thus causing the low-density urban sprawl of “ghost cities” (Rodrigue, 2020; Zheng et al., 2019).
The factors in HSR network attributes:
European experience showed that the more frequent the HSR service trains or the higher the centrality of the station in the HSR network, the more development of the station area was promoted (Wenner & Thierstein, 2022).
The longer HSR service years could motivate higher built-up land growth (Bellet & Ureña, 2016; Zhu et al., 2020).
Notes: Concerning the potential impact factors there are also so many built-up and non-built-up factors that could contribute different changes.
Generally, it can be categorized into three types of contributing factors: the factors in urban social economy, in HSR station location, and in HSR network attributes.

## Slide 7
Study Area
HSR stations in the Yangtze River Delta region
Location of research stations
Nanjing
(provincial capital city of Jiangsu Province)
Hangzhou
(provincial capital city of Zhejiang Province)
Shanghai
(municipality)
HSR lines | Year of opening | Length (km) | Station Counts
Shanghai-Nanjing HSR Line (SN HSR) | 2011 | 284 | 8
Shanghai-Nanjing Intercity Rail Line (SN Intercity) | 2010 | 301 | 19
Shanghai-Hangzhou HSR Line (SH HSR) | 2010 | 158 | 11
Hangzhou-Ningbo HSR Line (HN HSR) | 2013 | 150 | 5
Nanjing-Hangzhou HSR Line (NH HSR) | 2013 | 256 | 11
Ningbo
(prefecture-level city of Zhejiang Province)
1
2
3
4
5
Table. Information on five high-speed rail lines in the study area.
Types of the HSR station location with the urban built-up areas
29/50 stations
How many stations are there in each construction type?
2/50 stations
4/50 stations
15/50 stations
The construction of HSR lines in close proximity to the existing conventional railways and the upgrading of current conventional rail stations
The construction of new HSR lines outside the existing built-up area for the sake of line straightness and low construction cost
1
3
4
5
2
Notes: In the next part, let’s start with the study area.
Here listed the 50 HSR stations in the YRD region, which are located on five high-speed rail routes. These routes connect three provinces and 10 prefecture-level cities, representing one of the most economically active regions in China.
These 50 stations can be further divided into two construction types, with 15 stations upgraded from the current conventional rail stations, another 35 stations are newly built outside the existing built-up area, or far from the current rail stations.

## Slide 8
Data
Data categories and sources
Years: 2008 and 2020
Land cover types: impervious, greenfield, and water area.
I.
Landsat data
II.
High-Speed Rail Station data
(Data source: CLCD, annual China Land Cover Dataset,
with precision of 30 m * 30 m grid )
(Data source: openstreetmap.org, openrailwaymap.org)
HSR stations and
1-kilometer station catchment area
III.
Socioeconomic data
(Data source: census data, open map data, etc.)
At the city dimension:
GDP
Population
Radius of urban built-up area
Distance from HSR station to city center
……
At the station dimension:
HSR trains service frequency
HSR line numbers to the station
Urban rail line numbers to the station
Construction types of HSR station
……
Notes: The data used in our research contains three components: the Landsat Data, from the annual China Land Cover Dataset with precision of 30 m * 30 m grid;
the High-Speed Rail Station data, and the socioeconomic data of each HSR station and station city.

## Slide 9
Data
Metrics to evaluate land cover changes
R = 1 km
HSR station
Built-up area
Sample diagram of
1-km HSR catchment area
Changes in the size of built-up land (ΔBL)
The amount size of built-up land within the 1-kilometer catchment area of HSR station in 2008 and 2020.
 |  | (1)
Where, |  | 
 | denotes the amount of change in built-up land (BL) between 2020 and 2010 for station | 
 | denotes the built-up land (BL) in each pixel in 2020 for station | 
 | denotes the built-up land (BL) in each pixel in 2010 for station | 
 | denotes the number of pixels in the station area | 
 | denotes total land (TL) of the station area for station | 
 |  | (1)
Where, |  | 
 | denotes the number of pixels in the station area | 
Changes in the compactness degree (ΔCD)
To evaluate the composition urban compactness of the built-up land around the HSR stations.
 |  | (2)
 |  | (3)
Where, |  | 
 | denotes the compactness degree (CD) for station | 
 | denotes the change in compactness degree (CD) between 2020 and 2008 for station | 
 | denotes the Euclidean distance between each built-up land pixel to station | 
 | denotes the number of pixels in the station area | 
 | is a parameter for scaling to a value between 0 and 1 | 
 |  | (2)
 |  | (3)
Where, |  | 
 | denotes the number of pixels in the station area | 
A higher value of indicates a closer relationship between the built-up area and the HSR station, implying a better integration between land development and transport
1KM or 15-min walk
Notes: We developed three metrics to evaluate the land cover changes in the size of built-up land, the compactness degree, and the nighttime-light intensity.
The amount size of built-up land indicates how much the amount of built-up lands within the 1-kilometer catchment area of HSR station.
The compactness degree was designed to describe whether the built-up lands compactly distributed around the stations.

## Slide 10
Data
Metrics to evaluate land cover changes
R = 1 km
HSR station
Built-up area
Sample diagram of
1-km HSR catchment area
Changes in the nighttime-light intensity (ΔNI)
To evaluate the actual urban vitality around the station areas, indicating that to what extent the developed built-up area around the station could be effectively utilized.
 | (4)
 | (5)
 | (4)
 | (5)
Where, | 
 | denotes the night-time light intensity (NI) for station
 | denotes the night-time light intensity (NI) in each pixel for station
 | denotes the change in night-time light intensity (NI) between 2020 and 2010 for station
 | denotes the number of pixels in the station area
 | is a parameter for scaling to a value between 0 and 1
Where, | 
 | denotes the number of pixels in the station area
A higher value of indicates a more vibrant urban built-up area in the vicinity of HSR station, implying a better potential interaction between the station and the urban space.
Suzhou North Railway Station
2008
2020
Changes from 2008 to 2020
R = 1km
Green space
Water
Impervious (built-up area)
Newly built-up area
Notes: And the nighttime-light intensity was to describe the urban vitality around the station areas.
Here was an example of the land cover change of Suzhou North Railway Station, from 2008 to 2020. The purple color indicates the newly built-up lands within the 12 years, that is, converted from the greenfield to built-up lands.

## Slide 11
Descriptive analysis
Land cover changes in the station area
Indicators of change in built-up land | Min | Max | Mean | Standard Deviation
Changes in built-up land size () | 0.00 | 1.54 | 0.45 | 0.39
Changes in compactness degree () | 0.00 | 0.57 | 0.22 | 0.17
Changes in nighttime light intensity () | -0.06 | 0.65 | 0.18 | 0.14
Indicators of change in built-up land | Min | Max | Mean | Standard Deviation
 | 0.00 | 1.54 | 0.45 | 0.39
 | 0.00 | 0.57 | 0.22 | 0.17
 | -0.06 | 0.65 | 0.18 | 0.14
Table. Information on five high-speed rail lines in the study area.
Changes in the size of built-up land (ΔBL):
An average change area of BL: 0.45 km2.
The largest increment station area: Wuxi East (1.54 km2), Nanjing South (1.41km2), Suzhou New District (1.25 km2), Shaoxing East (1.08 km2), and Zhenjiang South (1.04 km2). – All the stations are the newly built stations.
The least increment station area: Shanghai Central (0.00 km2), Hangzhou Central (0.00 km2), Wuxi Central (0.002 km2). – All the stations are the upgraded stations.
Notes: These three figures showed the descriptive analysis in the three metrics we have just mentioned of the 50 HSR stations.

## Slide 12
Descriptive analysis
Land cover changes in the station area
Table. Information on five high-speed rail lines in the study area.
Changes in the compactness degree (ΔCD):
An average change level of CD: 0.22.
The stations with higher change level: Wuxi East (0.57), Nanjing South (0.54), and Suzhou New District (0.54). – All the stations are the newly built stations, indicating the development around the HSR stations within the 12 years are more compact.
The stations with lower change level: Shanghai Central (0.00), Hangzhou Central (0.00), and Wuxi Central (0.00). – All the stations are the upgraded stations, with less increment in the change level, but a relative initial compactness degree level in 2008.
Notes: Similarly, xxx

## Slide 13
Descriptive analysis
Land cover changes in the station area
Table. Information on five high-speed rail lines in the study area.
Changes in the compactness degree (ΔCD):
An average change level of CD: 0.22.
The stations with higher change level: Wuxi East (0.57), Nanjing South (0.54), and Suzhou New District (0.54). – All the stations are the newly built stations, indicating the development around the HSR stations within the 12 years are more compact.
The stations with lower change level: Shanghai Central (0.00), Hangzhou Central (0.00), and Wuxi Central (0.00). – All the stations are the upgraded stations, with less increment in the change level, but a relative initial compactness degree level in 2008.
Changes in the nighttime-light intensity (ΔNI):
An average change level of NI: 0.18.
The stations with higher change level: Shanghai Hongqiao (0.65), Suzhou North (0.58), and Changzhou North (0.36). – The development of the area around the station has implanted more types of urban activities and enhanced the vitality of the urban space.
The stations with lower change level: Shanghai South (-0.06), Wawushan (0.01), Xianlin (0.02). – After the completion of the HSR station, the vitality of the station area is reducing.
Notes: The results of nighttime-light intensity are quite different from the former two metrics.
It showed that Shanghai Hongqiao Railway Station gained the most vitalities within 12 years. And surprisingly, the vitality in Shanghai South Railway Station is reducing.

## Slide 14
Methodology: latent class analysis (LCA) with covariates
Model definition
Measurement model (right half part):
Direct involvement in the definition and delineation of the potential categories.
The indicators are directly observable variables used to define and differentiate potential categories.
The distribution pattern of these indicators determines the composition and characterization of potential categories.
Model of latent class analysis with covariates.
(indicators)
Structural model (left half part):
Influence the probability of each individual being assigned to a particular category through the logistic regression, etc.
The covariates are external variables used to predict and explain the probability of potential category membership.
They are not used directly to define categories, but rather to help the model understand what factors (certain of covariates) increase or decrease the probability of an individual belonging to a category.
Notes: About the methodology, the latent class analysis with covariates is mainly used in our study.
It consists of two model parts. The right part, also known as the Measurement Model, was to define and identify the latent classes of the samples.
Well, the left part, also known as the Structural Model, the three types of covariates were to explain the probability of potential category membership.

## Slide 15
Table. Descriptive statistics of covariates
Model parameters and results of LCA with covariates
Model parameters
Covariates (Attributes) | Min | Max | Mean | Standard Deviation
City socioeconomic attributes |  |  |  | 
GDP per capita in 2008 (hundred thousand RMB) | 0.31 | 2.19 | 0.64 | 0.34
Administrative level (Ref: municipality or provincial capital city) |  |  |  | 
prefecture-level city | 0 | 1 | 0.38 | 0.49
county-level city, district, or county | 0 | 1 | 0.40 | 0.49
HSR Station location attributes |  |  |  | 
Station location (dummy) |  |  |  | 
suburb (Ref: downtown) | 0 | 1 | 0.24 | 0.43
outskirts (Ref: downtown) | 0 | 1 | 0.36 | 0.48
Located in the metropolitan area (dummy) |  |  |  | 
yes (Ref: no) | 0 | 1 | 0.64 | 0.48
HSR network attributes |  |  |  | 
A newly built HSR station (dummy) |  |  |  | 
newly built station (Ref: upgraded station) | 0 | 1 | 0.70 | 0.46
Daily service trains (trains/day) | 5 | 729 | 124.24 | 158.39
Connected to urban rail transit networks (dummy) |  |  |  | 
yes (Ref: no) | 0 | 1 | 0.42 | 0.49
Distance to terminal HSR stations (hundred kilometers) | 0.001 | 1.65 | 0.58 | 0.46
HSR service years | 7 | 10 | 8.98 | 1.33
[Covariates]:
The covariates are external variables used to predict and explain the probability of potential category membership.
The relative distance from the HSR station to city center used as a quantitative basis:
Downtown: D/R <= 1.0
Suburb: 1.0 < D/R <= 1.8
Outskirts: D/R > 1.8
Notes: 讲的时候主要提mean，这代表有百分之多少的站点属于这个类型
About the results, it first listed the Descriptive statistics of nine covariates. And we can find from the table that, concerning the administrative level, 38% of the stations located in the prefecture-level city, 40% located in the county-level city, district, or county, and another 22% located in the municipality or provincial capital city.
The following can also be used to describe other variables in a similar way, so I will not go into the details here.

## Slide 16
Table. Latent class fit result for different classes number
Model parameters and results of LCA with covariates
Model results
When the class number is equal to two, the Bayesian Information Criterion (BIC) attains its minimum value and the degree of freedom of the model is non-negative.
Latent classes number | Degrees of freedom | AIC | BIC | X2 | Maximum log-likelihood
1 | 32 | 867.2965 | 901.7129 | 5491.597 | -415.6482
2 | 2 | 720.7796 | 812.5567 | 5442.16 | -312.3898
3 | -28 | 633.2266 | 782.3644 | 1216.677 | -238.6133
Figure. The box plan of three land cover change metrics of the HSR stations among the two latent classes.
Notes: The fit result of latent class analysis showed that the samples had the greatest distinctions when the latent clusters equals two.
And the bottom three figures exhibited the details of the land cover change between 12 years or the land cover benchmark levels.

## Slide 17
Model parameters and results of LCA with covariates
Model results
Class 1: urban renewal stations (N = 14, 28.0% of the total).
Acquired rarely in the ΔBL and ΔCD, but relative ΔNI within the 12 years.
With extremely high levels at all the three dimensions (BL, CD, & NI) in both 2008 and 2020.
Class 2: greenfield development stations (N = 36, 72.0% of the total).
The distinct high level increments in the 12-year interval at all the three dimensions.
The BL, CD, & NI in 2008 and 2020 were not as high as Class 1.
Typical HSR stations: Shanghai Central, Nanjing Central, Wuxi Central, Hangzhou East, Shanghai Hongqiao
Class 1: urban renewal stations (N = 14).
Class 2: greenfield development stations (N = 36).
The box plan of three land cover change metrics of the HSR stations among the two latent classes.
Typical HSR stations: Nanjing South, Suzhou North, Wuxi East, Huzhou Central
Notes: We can easily see from the figures that: the first group, that is, the red one, acquired rarely in the ΔBL and ΔCD, but relative ΔNI within the 12 years.
We can also find that these stations are initially with the extremely high levels at all the three dimensions in both 2008 and 2020. Some of the current conventional rail stations belong to the first group, we called it the Urban Renewal Stations.
The second group has distinct high level increments in the 12-year interval at all the three dimensions even if the initial level is relatively low in the three dimensions. We called it the Greenfield Development Stations. 36 out of 50 stations belong to this group.

## Slide 18
Model parameters and results of LCA with covariates
Contributing factors to land development patterns
The class 1, urban renewal stations, was selected as the reference for the sake of paying more attention to the station areas which are still growing.
Table. Latent class prediction of covariates.
[Reference category: Class 1 Urban renewal stations] (N = 50)
Class share (%) | Class 2: Greenfield development stations (72.0%) | 
Covariates | Coefficient | SE
Intercept | 19.803* | 5.284
Host city of the HSR station |  | 
GDP per capita in 2008 | -12.271 | 6.593
Administration level (Ref: municipality, and provincial capital city) |  | 
prefecture-level city | 3.730 | 2.823
county-level city, district, and county | 2.827*** | 0.269
HSR station location |  | 
Station location (Ref: downtown) |  | 
suburb | 9.505*** | 0.247
outskirts | 8.761*** | 0.062
Located in the metropolitan area (dummy) (Ref: no) | 6.628 | 5.233
HSR network attributes |  | 
Daily service trains | -0.013 | 0.038
A newly built HSR station (dummy) (Ref: upgraded station) | 17.028** | 2.652
Connected to urban rail transit networks (dummy) (Ref: no) | -8.741* | 2.475
Distance to terminal HSR stations | -5.796 | 3.955
Number of HSR service years | -18.317* | 5.881
Note: *, **, *** indicate statistical significance at 10%, 5%, and 1% level, respectively.
Contributing factors – Administration level
The stations located in county-level city, district, or county are more likely to be classified into Greenfield development stations, indicating that more increase in BL and CD mainly occurred at these administrative regions.
Contributing factors – HSR station location
The stations located at the suburb or outskirts are more likely to be classified into Greenfield development stations, exhibiting greater incremental built-up land but fewer improvements in nighttime light intensity and economic activities.
Contributing factors – HSR station construction types
Compared to the reference type, the newly built HSR stations have greater possibilities to belong to the Greenfield development stations.
In fact, among the 35 newly built HSR stations, only Shanghai Hongqiao Railway Station was classified into urban renewal stations. To some extent, it indicated that the development potential of the majority of newly built stations hasn’t been fully stimulated, with much lands could be further constructed.
Notes: This table reported the latent class prediction of covariates. The class 1, urban renewal stations, was selected as the reference for the sake of paying more attention to the station areas that are still growing.
Five types of covariates were verified to have impact on different classes.
As for the administration level, the stations located in county-level city, district, or county are more likely to be classified into Greenfield development stations.
Likewise, the stations located at the suburb or outskirts are similarly to be classified into Greenfield development stations.
Another finding was about the construction types. the newly built HSR stations have greater possibilities to belong to the Greenfield development stations.

## Slide 19
Model parameters and results of LCA with covariates
Contributing factors to land development patterns
Table. Latent class prediction of covariates.
[Reference category: Class 1 Urban renewal stations] (N = 50)
Class share (%) | Class 2: Greenfield development stations (72.0%) | 
Covariates | Coefficient | SE
Intercept | 19.803* | 5.284
Host city of the HSR station |  | 
GDP per capita in 2008 | -12.271 | 6.593
Administration level (Ref: municipality, and provincial capital city) |  | 
prefecture-level city | 3.730 | 2.823
county-level city, district, and county | 2.827*** | 0.269
HSR station location |  | 
Station location (Ref: downtown) |  | 
suburb | 9.505*** | 0.247
outskirts | 8.761*** | 0.062
Located in the metropolitan area (dummy) (Ref: no) | 6.628 | 5.233
HSR network attributes |  | 
Daily service trains | -0.013 | 0.038
A newly built HSR station (dummy) (Ref: upgraded station) | 17.028** | 2.652
Connected to urban rail transit networks (dummy) (Ref: no) | -8.741* | 2.475
Distance to terminal HSR stations | -5.796 | 3.955
Number of HSR service years | -18.317* | 5.881
Note: *, **, *** indicate statistical significance at 10%, 5%, and 1% level, respectively.
Contributing factors – Connected to the metro networks
The negative coefficient indicated that the HSR stations connected to the metro networks could obtained higher economic activity intensities, which are more likely to located in Urban renewal stations.
Contributing factors – HSR service years
The negative coefficient also showed that the station with longer HSR service tended to be equipped with the ability in accumulating urban vitalities, while the younger HSR stations were still in the stage of gathering new built-up lands.
It revealed that the longer HSR service was beneficial to form steady travel habit of using HSR trains. This travel behavior dependency was a positive effect for public amenities to gather around the stations.
Notes: The negative coefficient indicated that the HSR stations connected to the metro networks could obtained higher economic activity intensities, which are more likely to located in Urban renewal stations.
And so as the results in the HSR service years. The longer HSR service years tended to be equipped with the ability in accumulating urban vitalities.

## Slide 20
Discussion
Characteristics and planning strategies
50 HSR stations
in the YRD region
Urban Renewal Stations (14)
Greenfield Development Stations (36)
Indicators (6 metrics):
The changes level and benchmark level (2008) in BL, CD, & NI
Which includes:
13 upgraded conventional rail stations +
1 newly built station (Shanghai Hongqiao Rwy. Sta.)
Which includes:
34 newly built stations +
2 upgraded conventional rail stations
Besides, there are 11.4% of the newly built stations (4/35) failed to show a positive development potential in the station area.
Urban Renewal Stations (14):
The urban renewal stations could more easily be found at downtown area of the megacities.
The stations have more accumulations in urban activity densities and increment in land use intensities, and the increment on new construction lands seems to be not as essential.
Mainly upgraded from a conventional train station and connected to the metro network, indicating the megacities do have the willing and motivations to promote the urban renewal around the station, which has the favorable location conditions and opportunities.
Greenfield Development Stations (36):
The mainstream of the HSR station development patterns in our cases.
Most of which located in the suburb or the outskirts of the urban built-up area, especially in the counties or county-level cities.
Not all the newly built stations have been effective in orienting urban development. The greatest increments in the vicinity of the HSR stations could only be found in the intermediate stations of the megacities, like Suzhou, Wuxi, and Shaoxing, indicating the cautious decision-making in the integrated development of the stations and the small- and medium-sized cities.
Notes: As a consequence, we used the latent class analysis with covariates to identify the 50 HSR stations in the YRD region into two latent classes. 14 belongs to the Urban Renewal Stations, and the other 36 belongs to the Greenfield Development Stations.
The urban renewal stations could more easily be found at downtown area of the megacities. They have more accumulations in urban activity densities and increments in land use intensities. The majority of them are upgraded from the current conventional rail station, and connected to the metro network.
While the greenfield development stations are the mainstream of the HSR station development patterns in our cases. Most of them located in the suburb or the outskirts, especially in the counties or county-level cities. And we have also found Not all the newly built stations have been effective in orienting urban development.

## Slide 21
Conclusion
Differences with the previous findings:
The intermediate stations in megacities benefit most from the incremental built-up land size and compactness degree.
The terminal stations in megacities benefit most from the incremental urban vitality and land use intensities.
The relative distance to city center,
the construction types of HSR stations (upgraded or newly built),
as well as the administrative level of the stations have strong impacts on the land change patterns.
Our unique findings in this study:
Research contents:
The land composition of the built-up land around each HSR station was considered in our assessment framework, that is, the concept of compactness degree of built-up land as one of the essential indices.
All the upgraded and newly built HSR stations were considered into an integrated analysis framework in identifying the latent development patterns of the land cover change.
Methodology:
The latent class analysis with covariates were utilized in our research, with the amount, the composition, as well as the intensity of built-up land taken into consideration.
The location choice of HSR station and development plan of HSR new towns is a multi-objective decision-making process.
The promotion of HSR stations to urban development needs comprehensive and integrated urban systems to function, rather than the separated station buildings.
Notes: This is the last slide of our presentations. It was an early endeavor to investigate the land cover changes using the three dimensions of the amount, the composition, as well as the intensity.
Lastly, it also found that The location choice of HSR station and development plan of HSR new towns is a multi-objective decision-making process.
To promote the HSR stations as urban developments, it is essential to consider the integrated urban systems, instead of a separated station building.

## Slide 22
Identification of land cover change in high-speed rail (HSR) station area through latent class analysis with covariates:
Findings for the Yangtze River Delta region
Xinyi WANG (presenter) PhD candidate, Department of Urban Planning, Tongji University, China, xywang_@tongji.edu.cn
Haixiao PAN*, Ph.D. Professor, Department of Urban Planning, Tongji University, China, hxpank@126.com
Ya GAO, Ph.D. Postdoctoral Fellow, Department of Civil & Mineral Engineering, University of Toronto, Canada, lucia.gao@mail.utoronto.ca
Thank you and Q&A!
Forum THNS2024: TRANSFORMING TRANSPORT
Session 7: Transport and the environment
Notes: That is all of my presentation, thank you for listening, and I’d be happy to have and try my best to the questions., Thank you very much!

## Slide 23
Introduction
High-Speed Rail (HSR) and urban development
at inter-city spatial scale (more as a transit mode):
shrinking intercity spatio-temporal distance;
making intercity travel more frequent (Wenner and Thierstein, 2021).
at intra-city spatial scale (more as a catalyst for urban development):
HSR stations can also enhance economic activity in the areas adjacent to the stations;
indirectly impact the economic activities, population scale, or land development of various areas within a city by improving accessibility and spatial connectivity (Willigers & van Wee, 2011; Shen et al., 2017).
City A
City B
Station A
Station B
Station
City
Station area
City center/
Downtown
Sub-center
Sub-center
Metro lines
Transport-land use feedback cycle
(Source: Bertolini, 2012; Wegener et al., 1999; Dena et al., 2016)
Notes: Urban transport and land use are always in a dynamic cycle and feedback, so are the HSR system and urban space. At the intra-city scale, HSR stations can also enhance the economic activity in the areas adjacent to the stations or within the cities by improving the accessibility.

## Slide 24
Identifying Patterns
Analyzing Causes
Optimizing Systems
The land development changes in the 50 HSR station areas
METHOD
The latent contributing factors that affect the land development patterns
Descriptive Analysis: Developed three indices (the amount, compactness degree, and intensity of the built-up land) to describe the land development changes in 50 station areas.
Latent Class Analysis with Covariates: To identify the latent patterns of the land development changes among the 50 HSR stations considering the control of the covariates.
Latent Class Analysis with Covariates (aka Latent Class Regression): To explore the contributing factors that are conducive to different classes.
Policy Discussion: A multi-objective decision making based on the latent contributing factors to optimize the station area land development performance, and retrospect to the current HSR station planning.
Policy discussion and our contributions to the HSR station area development
STEP
CONTENT
Technical Route